SVD Notes and Scratchpad
(May 2018)
Mathematical Basics

Spectral Theorem:

M = UΣVT	(1)
U, V unitary, Σ diagonal.

Relationship to the eigenvalue decomposition of a symmetric matrix:

Let A := MMT
A is symmetric and positive semi-definite. → A is diagonalizable with nonnegative eigenvalues:
A = QDQT	(2)
Q unitary, D diagonal.

(1), (2): A = MMT = UΣVT VΣUT = UΣ2UT
→ UΣ2UT = QDQT
→ U = Q, Σ = D1/2 (D1/2 means replacing diagonal values of D with their square roots)

If all eigenvalues are positive, then VT = Σ-1UTM.
Else solve A’ := MTM = Q’D’Q’T producing V = Q’

Hence general SVD can always be reduced to the eigendecomposition of a positive semidefinite matrix. Since many use cases requiring SVD already start with a symmetric matrix, it is reasonable to just provide the eigendecomposition for the symmetric matrix (easier to maintain) rather than implementing general SVD. Any conceivable flavors of symmetric eigendecomposition should be faster than the corresponding flavor of general SVD, although applying above theorem for genral SVD might altogether be slightly slower than the best direct SVD implementation.

Eigendecomposition with Givens Rotation

c := cos(%theta) s := sin(%theta) G = G(k,l,%theta) : Givens Rotation

g_kl=s ; g_lk=-s ; g_kk = g_"ll" = c ; g_ij = %delta_ij forall i,j <> k,l

tilde A = AG^T ; A' = GAG^T = G tilde A

RAR^T = R'A' = R' GAG^T R'^T drarrow R = R' G drarrow R' = R G^T, R'^T = GR^T

Symmetry: a_ij = a_ji a'_ij = a'_ji forall i, j

a'_kl = a_kl(c^2-s^2) + cs (a_"ll"- a_kk)	(1)

a'_kk = a_kk c^2 + a_"ll" s^2 + 2 a_kl cs	(2)

a'_"ll" = a_kk s^2 + a_"ll" c^2 - 2 a_kl cs	(3)

For i,j <> k,l : a'_ik = a_ik c + a_il s , a'_il = a_il c - a_ik s	(4)

Rotation: q_ij := r^T_ij => q'_ki = c q_ki + s q_li , q'_li = c q_li - s q_ki

Jacobi Method

a'_kl = 0 => %theta = {1 over 2}tan^-1 left( { 2 a_kl } over { a_kk - a_"ll" } right) , c = cos( %theta ) , s = sin( %theta )

Givens Tridiagonalization

a'_{k-1,l} = 0 => (4) c a_{k-1,l} - s a_{k-1,k} = 0 drarrow %theta = tan^-1 left ( a_{k-1,l} over a_{k-1,k} right )

for(k = 1; k < n; k++)
for(l = k + 1; l < n; l++)
zero a_{k-1,l} , a_{l,k-1}

=> zeroed elements stay zero

Triangle Decomposition via Givens Rotation

c := cos(%theta) s := sin(%theta) G = G(k,l,%theta) : Givens Rotation

g_kl=s ; g_lk=-s ; g_kk = g_"ll" = c ; g_ij = %delta_ij forall i,j <> k,l

Q'A' = QA = Q G G^T A

=>

A' = G^T A

Q' = QG

a'_ij = sum from { { r = 0 } } to { n-1 } g^T_ir a_rj

a'_kj = sum from { { r = 0 } } to { n-1 } g^T_kr a_rj = g^T_kk a_kj + g^T_kl a_lj = c a_kj - s a_lj

a'_lj = sum from { { r = 0 } } to { n-1 } g^T_lr a_rj = g^T_lk a_kj + g^T_"ll" a_lj = c a_lj + s a_kj

Q'^T = G^T Q^T :

q'^T_kj = c q^T_kj - s q^T_lj

q'^T_lj = c q^T_lj + s q^T_kj

a'_kj = 0 drarrow c a_kj + s a_lj = 0 drarrow tan( %theta ) = a_kj / a_lj

A → upper triangular

for(l = 0; l < n; l++)
for(k = l + 1; k < n; k++)
zero a_{k, l}

A → lower triangular

for(l = n - 1; l >= 0; l--)
for(k = l - 1; k > 0; k--)
zero a_{k, l}

QR Cycle
Principle Idea: QR-Decomposition: A = QR (R = upper triangular).
QR Cycle: A’ := RQ = QTAQ
If A is symmetric and tridiagonal, Q has upper Hessenberg form (easily verifiable). Then RQ has upper Hessenberg form (product of upper triangle. & upper Hessenberg → upper Hessenberg). Since QTAQ is an orthogonal transformation of a symmetric matrix, A’ must be symmetric. From A’ also being upper Hessenberg follows that A’ must be tridiagonal.
→ QR Cycle Preserves Tridiagonality.
→ Only the tridiagonal elements of Q are actually needed for the computation.
→ O(n) effort per cycle. (O(n2) with updating rotation matrix)
Repeated cycles let A’ to converge to diagonal if sufficient gap between different eigenvalues.

Successive Givens rotations %theta_0, %theta_1, %theta_2, ... , %theta_i modifying row_i and row_{i+1} in ascending order such that r_{ i-1,i} = 0 . In the following notation we use h, i, j, k,l with h + 3 = i + 2 = j + 1 = k .
Matrix R
c_0 a_00 + s_0 a_01	c_0 a_01 + s_0 a_11	s_0 a_12	0
0	c_1( c_0 a_11 - s_0 a_01 ) + s_1 a_12	c_0 c_1 a_12 + s_1 a_22	s_1 a_23
0	0	c_2( c_1 a_22 - s_1 c_0 a_12 ) + s_2 a_23	c_2 c_1 a_23 + s_2 a_33
0	0	0	c_3( c_2 a_33 - s_2 c_1 a_23 ) + s_3 a_34

Generally:
s_j, c_j such that c_j a_jk = s_j ( c_i a_jj - s_i c_h a_ij )
r_jj = c_j( c_i a_jj - s_i c_h a_ij ) + s_j a_jk r_ij = c_h c_i a_ij + s_i a_jj r_ik = s_i a_jk
with c_j = 1 , s_j = 0 for j out of range {0, …, n-2}
Matrix QT
c_0	s_0	0	0
-s_0 c_1	c_0 c_1	s_1	0
not needed	-s_1 c_0 c_2	c_1 c_2	s_2
not needed	not needed	-s_2 c_1 c_3	c_2 c_3

Generally: q_jj = c_i c_j , q^T_jk = s_j , q^T_kj = -s_j c_i c_k
Matrix A’ = RQ
a'_ii = r_ii q^T_ii+r_ij q^T_ij = r_ii c_h c_i + r_ij s_i
a'_ij = r_ii q^T_ji + r_ij q^T_jj + r_ik q^T_jk = - r_ii s_i c_h c_j + r_ij c_i c_j + r_ik s_j

This operation can be implemented using the stack. (No extra heap memory needed)

Shifting
Alternative QR Cycle:
A’ = QTAQ = QT(A – λI )Q + λI
Q is chosen such that QT(A – λI ) is upper-triangular.
→ Convergence can be accelerated by strategically selecting λ for each iteration.
Method:
- Get eigenvalues of 2x2 sub-matrix of the last two columns and rows.
- Set λ to eigenvalue closer to the last diagonal element.
- Iterate until convergence
→ Test convergence by comparing last off-diag to last diag element.
→ Typically converges in 2...3 cycles. (A safety limit of 100 should be ample)
- Deflate matrix (from bottom) and repeat.

References
[1] Numerical Recipes in C (Pg. 456ff), ISBN 0-521-43108-5
[2] https://www.mathworks.com/content/dam/mathworks/mathworks-dot-com/moler/eigs.pdf
[3] Spectral Theorem: https://en.wikipedia.org/wiki/Spectral_theorem
[4] Spectral Decomposition: https://en.wikipedia.org/wiki/Matrix_decomposition
[5] https://en.wikipedia.org/wiki/Singular-value_decomposition