Modified Discrete Cosine Transform (MDCT) via Discrete Fourier Transform (DFT)

Johannes B. Steffens
Jan. 2022
Objective
The MDCT is a special transform from space- and/or time-domain into the frequency-domain. It was conceived in 1986 as part of an data compression methodology which ultimately resulted MPEG, OGG, H.263 and other audio and image/video compression standards.
The principal approach is subdividing the data stream in to blocks, transforming those blocks into the frequency domain (typically via DCT [2]), applying a perceptual salience-filter and disregarding all signals below a specified perception-level, with which the trade-off between compression rate and signal quality can be controlled. Decoding happens by applying the corresponding inverse transformations in reverse order.
Using isolated succeeding blocks introduces signal discontinuities during reconstruction. Those can be easily perceived in the time domain (less so in the space domain). This artifact is generally compensated by using overlapping blocks with a weighting scheme enforcing signal continuity. However, this harbors redundancies, thus reducing the compression efficiency.
The redundancy problem was eventually (very elegantly) solved in 1986 by conceiving the MDCT, which has the property that additional artifacts introduced by a forced critical sampling the frequency domain are automatically canceled in the overlapped reconstruction of the signal. The whole approach is known as "Time Domain Aliasing Cancellation" (TDAC) [3].
It is possible to express the DCT and especially MDCT in the form of a DFT with O(N) pre- and post-processing steps.
This document is a personal recap of the approach as baseline for designing/implementing space and time-domain compression algorithms.
MDCT
The MDCT defined on a block size of 2N with block-overlap N and block progression N:
X_k = sum from { { n = 0 } } to { 2N-1 } { x_n cos left(%pi over N left(n + 1 over 2 + N over 2 right) left( k + 1 over 2right) right) }{ } k in lbrace 0, ..., N-1 rbrace

The corresponding inverse transform IMDCT:
y_n = 1 over N sum from { { k = 0 } } to { N-1 } { X_k cos left(%pi over N left(n + 1 over 2 + N over 2 right) left( k + 1 over 2right) right) }{ } n in lbrace 0, ..., 2N-1 rbrace

Note that since MDCT is a projection setR^2N toward setR^N , the IMDCT can not immediately reproduce x_n . Instead it is
y_n = left lbrace binom {1 over 2 left ( x_n - x_{N-n} right ) for n in lbrace 0, ..., N - 1 rbrace} {1 over 2 left ( x_n + x_{2N-n} right ) for n in lbrace N, ..., 2N - 1 rbrace} right rbrace
One can show, however, that by applying the block-overlap on y_n with the same window-function (weighting function) with which x_n was obtained from the original samples, the original samples can be reconstructed exactly.
Applying the perceptual salience-filter in the frequency domain will introduce artifacts. However, these are effectively canceled with the reconstructing overlap calculation while the window function also tames any subsequent block-discontinuities.
MDCT via DFT
We describe the y_n = e ^{ { -i %pi n } over {2N} } " " DFT_n^2N left lbrace ..., X_k e ^ { { -i %pi left( (1 + N) (1 + 2k) right) } over {4N} },..., lbrace 0 rbrace^N right rbrace as DFT on the 2N block-size.
tilde X_k = sum from { { n = 0 } } to { 2N-1 } { tilde x_n e ^ { { -i %pi n k } over N } } = DFT_k^2N left lbrace ..., tilde x_n,... right rbrace
Without restricting generality, lets treat X_k, x_n as complex numbers and describe a complex MDCT as follows:
X_k = sum from { { n = 0 } } to { 2N-1 } { x_n e ^{ -i %pi over N left(n + 1 over 2 + N over 2 right) left( k + 1 over 2right) } }{ }
The relationship to the Real-MDCT can easily be seen by keeping "Re"(x_n) = 0 and disregarding "Im"(X_k) .
Separating the n*k mix term from other terms, we decompose the transformation to
X_k = e ^ { { -i %pi left( (1 + N) (1 + 2k) right) } over {4N} } " " sum from { { n = 0 } } to { 2N-1 } { x_n e ^{ { -i %pi n } over {2N} } e ^{ { -i %pi n k } over N } } for k in lbrace 0, ..., N-1 rbrace .
It follows a y_n = e ^{ { -i %pi n } over {2N} } " " DFT_n^2N left lbrace ..., X_k e ^ { { -i %pi left( (1 + N) (1 + 2k) right) } over {4N} },..., lbrace 0 rbrace^N right rbrace where only the left N output components are evaluated.
X_k = e ^ { { -i %pi left( (1 + N) (1 + 2k) right) } over {4N} } " " DFT_k^2N left lbrace ..., x_n e ^{ { -i %pi n } over {2N} }, ... right rbrace for k in lbrace 0, ..., N-1 rbrace

IMDCT via DFT
Analog to the above, we describe a complex IDCT as follows:
y_n = 1 over N sum from { { n = 0 } } to { N-1 } { "Re"(X_k) e ^{ -i %pi over N left(n + 1 over 2 + N over 2 right) left( k + 1 over 2right) } }{ } .
With the decomposition
y_n = 1 over N e ^{ { -i %pi n } over {2N} } " " sum from { { k = 0 } } to { N-1 } { "Re"(X_k) e ^ { { -i %pi left( (1 + N) (1 + 2k) right) } over {4N} } e ^{ { -i %pi n k } over N } } for n in lbrace 0, ..., 2N-1 rbrace ,
we get a DFT^2N with N right-padded 0s on the input vector:
y_n = 1 over N e ^{ { -i %pi n } over {2N} } DFT_n^2N left lbrace ..., "Re"(X_k) e ^ { { -i %pi left( (1 + N) (1 + 2k) right) } over {4N} },..., lbrace 0 rbrace^N right rbrace for n in lbrace 0, ..., 2N-1 rbrace .

References

[1]	Geiger et al. (2001). "Audio Coding Based on Integer Transforms."
(Paper: https://www.researchgate.net/publication/37380920_Audio_Coding_Based_on_Integer_Transforms)
(Full Thesis (2004)): https://www.db-thueringen.de/servlets/MCRFileNodeServlet/dbt_derivate_00013817/ilm1-2007000278.pdf)

[2]	N. Ahmed, T. Natarajan and K. R. Rao, "Discrete Cosine Transform," in IEEE Transactions on Computers, vol. C-23, no. 1, pp. 90-93, Jan. 1974, doi: 10.1109/T-C.1974.223784.

[3] J. Princen and A. Bradley, "Analysis/Synthesis filter bank design based on time domain aliasing cancellation," in IEEE Transactions on Acoustics, Speech, and Signal Processing, vol. 34, no. 5, pp. 1153-1161, October 1986, doi: 10.1109/TASSP.1986.1164954.